## Slide 1
AVR MICROCONTROLLER

## Slide 2: Microcontroller | AVR
The acronym of AVR stands for the initial AVR architecture designers: Alf-Egil Bogen & Vegard Wollen.
Statically sometimes it is elongated as Advance Virtual RISC.
Advance modified Harvard Architecture 8-Bit RISC single chip micro-controller
On-Chip a mini system
    On chip memory : Flash, SRAM, EEPROM
    I/O & multitasking Ports

## Slide 3: Microcontroller | AVR Architecture
Harvard Architecture:
  Separate Instruction and Data paths. Faster and simultaneous access to data and instructions.
  Pipelining Concept
RISC:
  Reduced Instruction Set computing rather than CISC i.e. x86
  Simpler Instructions execute faster
  Optimized most used instruction.

## Slide 4: Microcontroller | Program Memory Map
FLASH:
In system reprogrammable non-volatile program space storage is 8KB (for Atmega8) 16KB(Atmega 16). A separate memory space partitioned for Boot Flash section.
SRAM:
Temporary values, stack of volatile type memory, memory size 1KB
EEPROM:
512B of space availability storage space for long-term.

## Slide 5: Microcontroller | AVR Packages
PDIP:
Plastic dual-in-line Package abbreviated as PDIP is a chip-package with rectangular housing and two parallel rows of Electrical connecting pins.
TQFP:
Thin Quad Flat Package abbreviated as TQFP is a chip-package with quad housing with “gull wing” leads extending from each of four sides.

## Slide 6: | ATMEGA 8 |

## Slide 7: ATMega 8 | Features
ATmega 8 is a 28/32 Pin, 8 bit micro-controller based on AVR RISC Architecture.
The low-power Atmel 8-Bit AVR RISC based microcontroller combines 8KB of programmable flash memory, 1 KB of SRAM, 512K EEPROM.
Supports Harvard Architecture and single Level- Pipelining concept.
Operating Voltage : 2.7-5.5Volts
Complete System on a Chip :
On Board Memory ( FLASH, SRAM & EEPROM)
On Board Peripherals

## Slide 8: ATMega 8 | PINOUT
(RESET) PC6
(RXD) PD0
(TXD) PD1
(INT0) PD2
(INT1) PD3
(XCK/T0) PD4
Vcc
GND
(XTAL1/TOSC1) PB6
(XTAL2/TOSC2) PB7
(T1) PD5
(AIN0) PD6
(AIN1) PD7
(ICP1) PB0
PB1(OC1A)
PB2(SS/OC1B)
PB3(MOSI/OC2)
PB4(MISO)
PB5(SCK)
AVCC
AREF
GND
PC0(ADC0)
PC1(ADC1)
PC2(ADC2)
PC3(ADC3)
PC4(ADC4/SDA)
PC5(ADC5/SCL)

## Slide 9: ATMEGA 8 | Features
Atmel Atmega 8 is the heart of AVR Development Board
This 28 Pin microcontroller features 16 MIPS throughput capability at 16MHz. Although there is an internal Timer of 1 MHz which gives 1 MIPS.
I/O :
    Three Ports: PORT B , PORT C , PORT D of total 23 I/O Pins.
    ADC Pins : A0 to A5
    USART: PD0 (RXD) PD1(TXD)
    PWM: OC0A, OC1A, OC1B, OC2A, OC2B
Power: Chip operates in between 2.5V to 5.5V
PDIP type Atmega8

## Slide 10: ATMEGA 8 | Peripheral Features
PORT Features
    Two 8-bit Timer/Counters with Separate Prescalers and Compare Modes
    One 16-bit Timer/Counter with Separate Prescaler
    6 Channel 10 Bit Analog to Digital
    Master / Slave SPI serial interface
    Three PWM Channels
    Byte-oriented 2 Wire serial interface
    Programmable watchdog Timer
    Programmable Serial USART/UART

## Slide 11: | ATMEGA 16 |

## Slide 12: ATMEGA 16 | Features
Atmel Atmega 16 is a 40 Pin 16 KB In-System Self Programmable Flash Memory.
This microcontroller features 16 MIPS throughput capability at 16MHz. Although there is an internal Timer of 1 MHz which gives 1 MIPS.
I/O :
    Four Ports: PORTA , PORT B , PORT C , PORT D of total 32 I/O Pins.
    ADC Pins : A0 to A7
    USART: PD0 (RXD) PD1(TXD)
    PWM: Four PWM Channels
Power: Chip operates in between 2.5V to 5.5V
PDIP type Atmega16

## Slide 13: Microcontroller |PIN Diagram

## Slide 14: ATMega 16 | Features
PORT Features:
    Two 8-bit Timer/Counters with Separate Prescalers and Compare Modes
    One 16-bit Timer/Counter with Separate Prescaler
    8 Channel 10 Bit Analog to Digital
    Master / Slave SPI serial interface
    Four PWM Channels
    Byte-oriented 2 Wire serial interface
    Programmable watchdog Timer
    Programmable Serial USART/UART
    Programming of Flash, EEPROM, Fuses, and Lock Bits through the JTAG Interface

## Slide 15: Microcontroller | PDIP Vs TQFP